## Slide 1: MGT 207 Production and Operations Management
Process Strategy and Analysis

## Slide 2: Agenda
Process Strategies
  Process Focus, Repetitive Focus, Product Focus, Mass Customization
Process Investment
  Break-Even Analysis
Process Analysis
  Capacity
  Throughput
Notes: Add a slide on productivity etc. concepts in second hw problem

## Slide 3: Process Strategy
The objective is to create a process to produce offerings that meet customer requirements within cost and other managerial constraints

## Slide 4: Process, Volume, and Variety
Process Focus
projects, job shops (machine, print, hospitals, restaurants)
Repetitive
(autos, motorcycles, home appliances)
Harley-Davidson
Product Focus
(commercial baked goods, steel, glass, beer)
Frito-Lay
High Variety
one or few units per run,
(allows customization)
Changes in Modules
modest runs, standardized modules
Changes in Attributes (such as grade, quality, size, thickness, etc.)
long runs only
Mass Customization
(difficult to achieve, but huge rewards)
Dell Computer
Poor Strategy (Both fixed and variable costs are high)
Low Volume
Repetitive Process
High Volume
Volume
Figure 7.1
Variety (flexibility)

## Slide 5: Process Choice Based on Costs
Fixed vs. Variable Costs

## Slide 6: Crossover Chart Example
Evaluate three different accounting software products
Calculate crossover points between software A and B and between software B and C
 | TOTAL FIXED COST | DOLLARS REQUIRED PER ACCOUNTING REPORT
Software A | $200,000 | $60
Software B | $300,000 | $25
Software C | $400,000 | $10

## Slide 7: Crossover Charts
Fixed costs
Variable costs
$
High volume, low variety
Process C
Fixed costs
Variable costs
$
Repetitive
Process B
Fixed costs
Variable costs
$
Low volume, high variety
Process A
Fixed cost Process A
Fixed cost Process B
Fixed cost Process C
Total process A costs
Total process B costs
Total process C costs
V1
(2,857)
V2
(6,666)
400,000
300,000
200,000
Volume
$
Figure 7.3

## Slide 8: Process Choice Based On Capacity
Bottleneck Analysis

## Slide 9: Outline
Capacity
Bottleneck Analysis and the Theory of Constraints

## Slide 10: Capacity
The throughput, or the number of units a facility can hold, receive, store, or produce in a period of time
Determines fixed costs
Determines if demand will be satisfied
Notes: This slide provides some reasons that capacity is an issue. The following slides guide a discussion of capacity.

## Slide 11: Design and Effective Capacity
Design capacity is the maximum theoretical output of a system
  Normally expressed as a rate
Effective capacity is the capacity a firm expects to achieve given current operating constraints
  Often lower than design capacity
Notes: This slide can be used to frame a discussion of capacity.
Points to be made might include:
- capacity definition and measurement is necessary if we are to develop a production schedule
- while a process may have “maximum” capacity, many factors prevent us from achieving that capacity on a continuous basis.
Students should be asked to suggest factors which might prevent one from achieving maximum capacity.

## Slide 12: Design and Effective Capacity
TABLE S7.1 | Capacity Measurements |  | 
MEASURE |  | DEFINITION | EXAMPLE
Design capacity |  | Ideal conditions exist during the time that the system is available | Machines at Frito-Lay are designed to produce 1,000 bags of chips/hr., and the plant operates 16 hrs./day. Design Capacity = 1,000 bags/hr. × 16 hrs. = 16,000 bags/day
Notes: This slide can be used to frame a discussion of capacity.
Points to be made might include:
- capacity definition and measurement is necessary if we are to develop a production schedule
- while a process may have “maximum” capacity, many factors prevent us from achieving that capacity on a continuous basis.
Students should be asked to suggest factors which might prevent one from achieving maximum capacity.

## Slide 13: Design and Effective Capacity
TABLE S7.1 | Capacity Measurements |  | 
MEASURE |  | DEFINITION | EXAMPLE
Effective capacity |  | Design capacity minus lost output because of planned resource unavailability (e.g., preventive maintenance, machine setups/changeovers, changes in product mix, scheduled breaks) | Frito-Lay loses 3 hours of output per day (= 0.5 hrs./day on preventive maintenance, 1 hr./day on employee breaks, and 1.5 hrs./day setting up machines for different products). Effective Capacity = 16,000 bags/day – (1,000 bags/hr.) (3 hrs./day) = 16,000 bags/day – 3,000 bags/day = 13,000 bags/day
Notes: This slide can be used to frame a discussion of capacity.
Points to be made might include:
- capacity definition and measurement is necessary if we are to develop a production schedule
- while a process may have “maximum” capacity, many factors prevent us from achieving that capacity on a continuous basis.
Students should be asked to suggest factors which might prevent one from achieving maximum capacity.

## Slide 14: Design and Effective Capacity
TABLE S7.1 | Capacity Measurements |  | 
MEASURE |  | DEFINITION | EXAMPLE
Actual output |  | Effective capacity minus lost output during unplanned resource idleness (e.g., absenteeism, machine breakdowns, unavailable parts, quality problems) | On average, machines at Frito-Lay are not running 0.25 hr./day due to late parts and machine breakdowns. Actual Output = 13,000 bags/day – (1,000 bags/hr.) (0.25 hr./day) = 13,000 bags/day – 250 bags/day = 12,750 bags/day
Notes: This slide can be used to frame a discussion of capacity.
Points to be made might include:
- capacity definition and measurement is necessary if we are to develop a production schedule
- while a process may have “maximum” capacity, many factors prevent us from achieving that capacity on a continuous basis.
Students should be asked to suggest factors which might prevent one from achieving maximum capacity.

## Slide 15: Utilization and Efficiency
Utilization is the percentage of design capacity actually achieved
Efficiency is the percentage of effective capacity actually achieved
Utilization = Actual output/Design capacity
Efficiency = Actual output/Effective capacity

## Slide 16: Bakery Example
Actual production last week = 148,000 rolls
Effective capacity = 175,000 rolls
Design capacity = 1,200 rolls per hour
Bakery operates 7 days/week, three 8-hour shifts
Design capacity = (7 x 3 x 8) x (1,200) = 201,600 rolls
Design Capacity
Notes: It might be useful at this point to discuss typical equipment utilization rates for different process strategies if you have not done so before.

## Slide 17: Bakery Example
Actual production last week = 148,000 rolls
Effective capacity = 175,000 rolls
Design capacity = 1,200 rolls per hour
Bakery operates 7 days/week, 3 - 8 hour shifts
Design capacity = (7 x 3 x 8) x (1,200) = 201,600 rolls
Utilization = 148,000/201,600 = 73.4%
Utilization
Notes: It might be useful at this point to discuss typical equipment utilization rates for different process strategies if you have not done so before.

## Slide 18: Bakery Example
Actual production last week = 148,000 rolls
Effective capacity = 175,000 rolls
Design capacity = 1,200 rolls per hour
Bakery operates 7 days/week, 3 - 8 hour shifts
Design capacity = (7 x 3 x 8) x (1,200) = 201,600 rolls
Utilization = 148,000/201,600 = 73.4%
Efficiency = 148,000/175,000 = 84.6%
Efficiency
Notes: It might be useful at this point to discuss typical equipment utilization rates for different process strategies if you have not done so before.

## Slide 19: Bakery Example
Actual production last week = 148,000 rolls
Effective capacity = 175,000 rolls
Design capacity = 201,600 rolls per line
Efficiency = 84.6%
Design capacity = 201,600 x 2 = 403,200 rolls
Expected output of new line = 130,000 rolls
Design Capacity
Expansion
Notes: It might be useful at this point to discuss typical equipment utilization rates for different process strategies if you have not done so before.

## Slide 20: Bakery Example
Actual production last week = 148,000 rolls
Effective capacity = 175,000 rolls
Design capacity = 201,600 rolls per line
Efficiency = 84.6%
Design capacity = 201,600 x 2 = 403,200 rolls
Expected output of new line = 130,000 rolls
Effective capacity = 175,000 x 2 = 350,000 rolls
Effective
Capacity
Expansion
Notes: It might be useful at this point to discuss typical equipment utilization rates for different process strategies if you have not done so before.

## Slide 21: Bakery Example
Actual production last week = 148,000 rolls
Effective capacity = 175,000 rolls
Design capacity = 201,600 rolls per line
Efficiency = 84.6%
Design capacity = 201,600 x 2 = 403,200 rolls
Effective capacity = 175,000 x 2 = 350,000 rolls
Expected output of new line = 130,000 rolls
Actual output = 148,000 + 130,000 = 278,000 rolls
Actual Output
Expansion
Notes: It might be useful at this point to discuss typical equipment utilization rates for different process strategies if you have not done so before.

## Slide 22: Bakery Example
Actual production last week = 148,000 rolls
Effective capacity = 175,000 rolls
Design capacity = 201,600 rolls per line
Efficiency = 84.6%
Design capacity = 201,600 x 2 = 403,200 rolls
Effective capacity = 175,000 x 2 = 350,000 rolls
Actual output = 148,000 + 130,000 = 278,000 rolls
Utilization = 278,000/403,200 = 68.95%
Efficiency = 278,000/350,000 = 79.43%
Expected output of new line = 130,000 rolls
Utilization
Efficiency
Expansion
Notes: It might be useful at this point to discuss typical equipment utilization rates for different process strategies if you have not done so before.

## Slide 23: Managing Capacity and Demand
Demand exceeds capacity
  Curtail demand by raising prices, scheduling longer lead times, discouraging marginally profitable business
  Long-term solution is to increase capacity
Capacity exceeds demand
  Stimulate market
  Product changes
Adjusting to seasonal demands
  Produce products with complementary demand patterns

## Slide 24: Process Analysis
Determine system capacity and throughput time
  Panda Express wants to know how many customers they can serve in a day
  Amazon is interested in learning how many packages they can process and ship from its warehouses
Identify bottlenecks in a process and understand how to manage them

## Slide 25: Capacity and Throughput
Maximum average output rate (output/unit time) that the system can maintain under normal conditions
Time required to get through the entire process from start to end
Capacity
Throughput time
(Flow time)
Average rate units actually being processed (output/unit time)
Throughput
Throughput is Less Than or Equal to Capacity
Time required to produce a unit at a workstation
  Subways have three work stations
Process time
Notes: Capacity: the maximum productive capability of a process or facility, usually measured as a quantity of output per unit time (rate).
How many of you would agree with that flow time is a measure of capacity? No it is not. CAPACITY IS ALWAYS A RATE!!

## Slide 26: What is a Bottleneck?
The step in the production/service delivery process:
a) that has the lowest capacity when measured
using a comparable unit of measure and, therefore,
b) that limits the overall output of the system.
Bottleneck
Definition
a) On paper: Determine the capacity - using a comparable measure - of each step in the process.
b) Line of sight: Find the place in the production process that has the highest level of Work-In-Process (WIP) inventory.
How Do You
Find A
Bottleneck?
Notes: Focus the story with an example - say a steel mill - that involves several steps.
Some steps operate at a high processing rate, others at a low processing rate. Somewhere, in the process, one or more of those steps are dragging down the production rate - i.e. the slowest ones. They are the bottlenecks.
Focus on issue of comparable units of measure.

## Slide 27: Capacity Analysis
Wrap/
Deliver
37.5 sec/sandwich
Order
30 sec/sandwich
Bread
Fill
15 sec/sandwich
20 sec/sandwich
Toaster
40 sec/sandwich
Assembly line
Instead, we can convert processing times (sec/sandwich) to capacity of the individual stages (e.g. sandwiches/hr) and pick the stage with the lowest capacity

## Slide 28: Capacity Analysis: Parallel Processes
Wrap/
Deliver
37.5 sec/sandwich
Order
30 sec/sandwich
Bread
Fill
15 sec/sandwich
20 sec/sandwich
40 sec/sandwich
Bread
Fill
Toaster
15 sec/sandwich
20 sec/sandwich
Toaster
40 sec/sandwich
First assembly line
Second assembly line
sec/sand
sec/sand
sec/sand
Has the capacity of the restaurant doubled after doubling the capacity of the (previous) bottleneck?

## Slide 29: Example 1 (1 of 4)
Keith’s Car Wash offers two types of washes: Standard and Deluxe. The process flow for both types of customers is shown in the following chart. Both wash types are first processed through steps A1 and A2. The Standard wash then goes through steps A3 and A4 while the Deluxe is processed through steps A5, A6, and A7. Both offerings finish at the drying station (A8). The numbers in parentheses indicate the minutes it takes for that activity to process a customer.
Figure 6.1 Process Flow for Keith’s Car Wash

## Slide 30: Q1
Q: Which step is the bottleneck for the Standard car wash process? For the Deluxe car wash process?
A: Step A4 is the bottleneck for the Standard car wash process, and Step A6 is the bottleneck for the Deluxe car wash process, because these steps take the longest time in the flow.

## Slide 31: Q2
Q: What is the capacity (measured as customers served per hour) of Keith’s Car Wash to process Standard and Deluxe customers? Assume that no customers are waiting at step A1, A2, or A8.
A: The capacity for Standard washes is 4 customers per hour because the bottleneck step A4 can process 1 customer every 15 minutes. The capacity for Deluxe car washes is 3 customers per hour.

## Slide 32: Q3
Q: If 60 percent of the customers are Standard and 40 percent are Deluxe, what is the average capacity of the car wash in customers per hour?
A: The average capacity of the car wash (0.6 x 4)+(0.4 x 3) = 3.6 customers per hour

## Slide 33: Q4
Q: Where would you expect Standard wash customers to experience waiting lines, assuming that new customers are always entering the shop and that no Deluxe customers are in the shop? Where would the Deluxe customers have to wait, assuming no Standard customers?
A: Standard wash customers would wait before steps A1, A2, A3, and A4 because the activities that immediately precede them have a higher rate of output (i.e., smaller processing times). Deluxe wash customers would experience a wait in front of steps A1, A2, and A6 for the same reasons. A1 is included for both types of washes because the arrival rate of customers could always exceed the capacity of A1.

## Slide 34: Drum-Buffer-Rope Systems (1 of 3)
Drum-Buffer-Rope
A planning and control system that regulates the flow of work-in-process materials at the bottleneck or the capacity constrained resource (C C R) in a productive system

## Slide 35: Drum-Buffer-Rope Systems (2 of 3)
The bottleneck schedule is the drum because it sets the beat or the production rate for the entire plant and is linked to market demand.
The buffer is the time buffer that plans early flows into the bottleneck and thus protects it from disruption.
The rope represents the tying of material release to the drumbeat, which is the rate at which the bottleneck controls the throughput of the entire plant.
Buffer management constantly monitors the execution of incoming bottleneck work.

## Slide 36: Drum-Buffer-Rope Systems (3 of 3)
Figure 6.3 Drum-Buffer-Rope System

## Slide 37: Summary
A bottleneck is a point in the production process where work slows down or stalls, creating a constraint on the overall flow. It's like the narrowest part of a bottle – it determines the maximum rate at which liquid can flow out.
Bottlenecks can occur anywhere in the production chain, from machines breaking down to inefficient processes or even a lack of skilled labor.
Identify the bottleneck: Thoroughly analyze your production process to pinpoint where the slowdown is occurring.